Website:  www.aerobiology.net

BULK, Test Code 2302-Endotoxin Analysis

Endotoxins are produced by gram negative bacteria and found on the outer membrane of the bacteria. Gram negative bacteria are common in the environment and have been associated with various respiratory symptoms and indoor complaints. Fever, headaches, nausea, and difficulty breathing are just some symptoms of exposure to endotoxins. Ventilation systems and humidifiers are a source for gram negative rods. Water damaged building material, metal working machines, and recirculated water systems can also be expected to have gram negative bacteria.

For bulk sampling, endotoxin free cassettes are available thru Aerobiology. The flow rate should be set at 10-15 l/min and run for at least 5 minutes.  The laboratory needs about 0.1 grams or more of dust for the analysis.  Do not touch the openings around the cassette because you will contaminate the cassette.

1.   Calibrate the pump to 15-20 L/min.

2.   Wearing gloves, attach the cassette to pump and begin vacuuming area. *Remember the lab needs 0.1 grams or more of dust for a sufficient sample.

3.   When done sampling replace cap on cassette.

4.    Place cassette in plastic bag then a box for shipping with Chain of Custody.

5.    Sample should be sent overnight to the laboratory for analysis.

References:

Dillon, H. Kenneth, L. Hung, J. Miller, Field Guide for the Determination of Biological Contaminants in Environmental Samples., 7.5 (2005).

Macher, Janet, Sc.D., M.P.H., Bioaerosols , 23.1-23.7.4 (1999).

43760 Trade Center Place, Suite 100, Dulles, VA 20166 (703) 648-9150 Fax (703) 648-0963 e-mail: lab@aerobiology.net

4501 Circle 75 Parkway, Ste A1190, Atlanta GA 30339 (770) 947-2828 Fax (770) 947-2938 e-mail: ATL@aerobiology.net